Automatic Cat Feeder.
A consumer device to assist in owning pets.

Matthew Smith
Chris Ranc
Shabab Siddiq

Component Description: Food dispensing unit.
Author: Matthew Smith
Date: 7-11-2017

Overview:
As a Computer Engineering project, one extremely important aspect of a physical design that carries the most risk is the actual method of dispensing food. As a dispensing unit, the design must be able to hold several days worth of food and be able to dispense without jamming or crushing the food. This design needs to be free of obstructions that would restrict food flow as well. Since the food will be gravity fed, we will also need to ensure that the assembly is not too top heavy such that it’d fall over with little effort.

Risk Specification

Needs:
1- multi day food supply
2- reliable portion control
3- non destructive dispensing

engineering specs:
1-large tapered container to hold food
2-”high resolution” dispensing that doesn’t dump food into a bowl
3-reduction of areas where dispenser could bind, causing damage to the system or to the food

Since the idea of an automatic pet feeder is to reduce how often one must feed their animals, it’s important to have some sort of multi day food supply as otherwise the owner might as well directly feed his or her animals directly, if the feeder must be fed daily anyway.

It’s important to be able to control portions, even if not fully precise. Different animals are different sizes and need different amounts of food. This should be able to be done in a controlled manner.

Any area where food can get stuck could lead to long term reliability concerns. These should be mitigated to the best of ones ability to provide the best product possible.

Risk investigation:

Survey of existing systems/components:

Cereal dispenser:
Pros:
-Dispenses dry goods as the main point of design
-easy to adapt to be motorized
-Complete assembly includes food container, top, elevated base, and dispensing controls

Cons:
-somewhat expensive
-dispenses via paddles. This works for cereal when attempting to fill a bowl but has too
much variation in how much is dispensed.
-paddles create points for dry food to bind and stop dispensing. Requires intervention	from operator to rotate back and forth to free bind.

Screw based dispenser:
Pros:
-Dispenses food in fine grain amounts allowing control over how much is fed
- less binding points
-easy to drive with a motor/servo

Cons:
-must source upper container and modify to feed food properly into screw opening.
-more time spent designing screw that would reduce binding.
-still requires intervention with binding, just less.

Trap door dispenser
Pros:
-Extremely mechanically simple
-durable
-no worry about binding.

Cons:
-Very little control over amount released
-bulky compared to rotating assemblies.

Concepts considered and chosen

One of the most important features of the design to consider when choosing a dispensing method is the ability to properly portion. Since one of the main features of this product is portion control and ability to cater to the needs of different animals, precise control is the first priority. Because of this, the trap door would immediately be eliminated.
Second, it is important to reduce the amount of food to be crushed during the dispensing. This is important to ensure the safety of the food from possible residual bacteria, as well as ensuring long term durability. Both the screw based dispensing and the paddle mechanism from the cereal dispenser have the ability to bind when food pieces fall into the wrong position. For the screw design, this can be mitigated via a combination of hopper design and screw design. The paddle based design is relatively simple and requires that falling food fall into a sharp “V” shape that when totally full, creates a pile of food that could cause binding while turning. This can be seen in the illustration in Figure 1.