Automatic Cat Feeder.
A consumer device to help alive the chore of owning pets.

Dispensing Unit: Investigation into the physical design of the food dispensing unit.

Author: Matthew Smith
Team Member: Chris Ranc
Team Member: Shabab Siddiq
Submission Date: 11-7-2017
Table of contents

Overview:
As a Computer Engineering project, one extremely important aspect of a physical design that carries the most risk is the actual method of dispensing food. As a dispensing unit, the design must be able to hold several days worth of food and be able to dispense without jamming or crushing the food. This design needs to be free of obstructions that would restrict food flow as well. Since the food will be gravity fed, we will also need to ensure that the assembly is not too top heavy such that it’d fall over with little effort.

Risk Specification

Market Requirements	Engineering Requirement	Justification
	A. An automatic feeder should be able to hold a multi-day supply of pet food.	In order to justify an automatic feeder, the user must not need to tend to the feeder often.
	B. Portion control for the feeder must be reliable and reasonably precise.	In order for the feeder to suit the needs of a diverse group of pets, the portions need to be controllable to accommodate size and health restrictions.
	C. Dispensing mechanism must be reliable enough to not jam or crush food too often.	It’s important that the unit does not jam because it’s designed to be trusted to feed while the owner is away for a reasonable time. A jam could mean a day without being fed.

Risk investigation:

Survey of existing systems/components:

In order to have a cohesive system, the container must taper into a hopper that then feeds into the chosen dispensing mechanism. This means the hopper must be designed around the dispensing mechanism. As this mechanism carries the responsibility of both reliably and precisely dispensing food, it will be the primary focus of this investigation. Many future aspects of the design will be dependent on how food is dispensed from the unit, making this the lynch pin in the design.

When beginning to design and search for solutions, it’s often a good idea to look at solutions that already exist on the market for inspiration as well as learning based on others’ past decisions, productive or otherwise. A very common consumer item that was designed to specifically dispense dry goods is the cereal dispenser. These are often seen in hotels to provide varying kinds of cereal to patrons. These devices are manually controlled by a knob in the front that rotates a four-paddle assembly that allows cereal to fall into a “V” shaped area, then the assembly rotates to drop the cereal down into a bowl below. This is a very common design due to the simplicity and the use cases associated with it. This design is particularly good at dumping larger servings into the bowl with the goal of filling it, but does not provide much room for precise control. This design also has a tendency to bind while rotating and in turn, pulverizing the dry food caught up. An illustration of this can be seen in Figure 1 in the appendix. This is often solved by the intelligent human operator rotating the assembly in the reverse direction then back in the original direction to clear the bind. With the intelligent user being replaced by an electric motor, the possible binding risks long term reliability on the design.

Another possible method seen in other dry goods dispensers is the simple trap door design. This idea can take many forms and orientations to allow food to spill out. This design is also very simple to implement. Similar to the paddle-based design, this method has trouble with precise dispensing. Unlike the paddle-based design, binding is rarely an issue due to the nature of an opening and closing door. It is possible that the door used in conjunction with a secondary dispensing method would allow to reduce the force of food stacked above the mechanism and by relation, reduce or remove possible binding. This possibility will need to be investigated further as well.

A third design possibility is not often seen in the context of moving dry food but is very common in automation applications such as injection molding, where a precise amount of material must be fed and injected into a mold. This design uses a a screw embedded into a tube that would allow for food to fall into the tube and the screw would rotate and push it along. The screw would be installed on an axle that could be easily driven by a motor. Since the screw would only allow small amounts of food to fall between threads and pushed forward by the screw rotating, thus advancing the food to the drop point. This allows for the speed and the amount of food dispensed to be controlled with a far greater amount of precision. The downside to the screw based dispenser mechanism is that great care will be involved in designing the screw and hopper, particularly the angle of attach on the threads and the taper of the hopper. Any sort of binding could be greatly mitigated with a proper design, compared to the nature of the paddle dispenser that has far less room for improvement compared to the screw design.

Concepts considered and chosen:

First and foremost, the final design should be able to reliably portion and control the output of the pet food. Due to this, the most important design decision will be based on the mechanism that controls this. From research into feed methods, the screw design beats out other considered methods by a long shot in it’s ability to portion food in a semi controlled resolution compared to how the paddles and doors mostly dump the food.

Another point to consider is the durability of the design. For the paddle design, if a bind is encountered, a greater amount of torque would be needed for the paddle to overcome the bind compared to the screw. The screw can also be designed in such a way that the binding point would be far smaller. Another property of the mitigated screw design is that with a shallow angle of attack on the screw allows for food to be pushed back into the next gap between threads rather than getting stuck right away. Overall, the screw design, while being the more difficult design, can do the job of the dispensing mechanism the best out of other possible designs.

Risk Mitigation Design

The most important aspect of the design being considered is the ability to portion food. Therefore the best choice for the dispensing mechanism is the feed screw design. With this choice the remainder of the dispenser can be designed around it. The overall design will be a vertical, gravity fed container to act as a hopper to feed into the feed screw. The feed screw will be held in a well fitting tube with a large enough tolerance allow dust past the edges. The tube under the hopper will be cut to allow food to enter and the end will be open to allow for the food to fall. The feed screw will be driven by a stepper motor to allow for precise control of the feed screw rotation. This will be constructed on an elevated base to allow for food to fall into the bowl.

The first focus of this design will be in the feed screw itself. A feed screw is a common design that is used in many applications including material extractions. It is very similar to a drill or auger in most ways except in that the feed screw remains stationary while augers or drills move. Since feed screws are relatively common of a design, it can be easy to find many examples online. For the purpose of a prototype and the lack of considerable modeling experience, open source designs will be used as a jumping off point towards creating a working prototype. One particular design found provided the same service as this project, albeit far more simple and static in configuration. This design used a 3d printed auger within a PVC tube and fed by a plastic container. This 3D auger design can be modified to fit the scale of this design and be made to fit the motor of our choice. A 3D rendering of this design can be seen in Figure 2. This source project can be found in the appendix.

Using this feed screw/auger design. Material must be selected for the outer tube. The original application called for a 1.5’’ female PVC T coupling. Since The inner diameter of this fitting is the outer diameter of standard PVC, the design will likely need to be modified to fit a standard sized piece of tubing. It would be beneficial to use a standard size pipe with a smooth interior to reduce and mitigate any possible binding that could be caused by a rough surface. PVC is also commonly used in water and food applications, making it a safe choice to use with food. It will still be important to have clean cuts and wash after working on it to ensure nothing could get into the animals food.

In order to drive this feed screw, an electric motor with both feedback and continuous rotation will be needed. A simple DC motor does not have the ability to know its rotational position and would not be a good choice for driving something where you need fine control. A servo can be aware of position, but a continuous servo loses that ability and is just a geared motor. A stepper motor can have fine grain control over movement with the ability to rotate continuously in a single direction. The torque requirements of the stepper motor is currently unknown, therefore specific decisions on motors and belt/pulley configurations are currently unknown as well. Is known that additional electronics will be needed to drive a stepper motor using a micro controller. This will be a consideration for later in the design and is not within the scope of this investigation.

Finally, the hopper/food container can be made from durable acrylic panels. These panels can be cut to construct a proper taper at the bottom of the hopper to ensure smooth feeding. The acrylic can be constructed via screws and pre-drilled holes, combined with a glue to seal it. This will result in a strong and safe container for an animal’s food to be held. A cover can be constructed in the same fashion to prevent foreign objects from falling in.

 With proper clearances, this design will be able to avoid most binding while being powerful enough to push the food. The feeder screw allows for fine control due to how it releases small amounts of food per revolution. With a smooth outer tube and a correct blade angle, binding should be rare. This setup allows for food to be filled high in the hopper, supporting a multi-day food supply.

<risk subsystem diagrams>

<Detailed Design>

In searching for patents of a similar design, one patent, US 6401657 B1, was found to be similar but not nearly identical in form or purpose. This device uses a very common auger feed delivery system but the bowl is integrated in the unit. It does not extend to the extended functionality of the design.

Parts List

3d printed feed screw
3D printed base
misc 3d printed fittings and adapters
stepper motor $15-20 available now
stepper motor driver $5-10
PVC pipe $1-5 dollars
acrylic 5-10 dollars
screws 3 dollars
glue 5 dollars

Testing strategy
Initial testing will consist of verification of the main functionality. The feeder dispenser should be able to reliably dispense food under it’s own power in small enough increments that would allow for proper portion control. Once the mechanism is functional alone, it can then be integrated into any driving logic from installed micro-controllers. Paired with the micro-controller, automatic feeding will be tested with several refills to ensure functionality. Within these tests, portions will be weighed and recorded to ensure consistent portions. If at one point this fails to be reliable, certain aspects of the design may need to be revisited. As hardware is the most difficult to make rapid changes to, much care will go into the design and functionality will be checked as early in the revision as reasonably possible.

Uncertainties

Appendix